## Slide 1: Signal Processing in the ProtoDUNE-SP LArTPC
Wenqiang Gu
Brookhaven National Laboratory
For the DUNE collaboration

## Slide 2: ProtoDUNE Single Phase (SP)
A 0.77-kt LArTPC at the CERN Neutrino Platform (NP)
  World largest monolithic single-phase LArTPC
Prototypes DUNE far detector (FD) components design at 1: 1 scale
Started operation in late 2018
  Exposed to cosmic & a dedicated charged particle beam (0.3 - 7 GeV)
similar energy to ’s interaction in DUNE
E.M. shower
T12.00005, Hannah Elizabeth Rogers
Overview of ProtoDUNE and Initial Study of Space Charge

## Slide 3: ProtoDUNE-SP Overview
7.2m
7m
6m
60 Photon Detectors
  Light collecting bars read out by SiPMs installed in the APA frame (10 detectors/APA)
  3 distinct versions installed → testing solutions for DUNE
L17.00004, Bryan J Ramson
The Photon Detection System (PDS) at ProtoDUNE
6 Anode Plane Assemblies (APAs)
  Total 15,360 TPC sense wires/channels with ~ 5mm pitch
  99.74%: active channels
3 Cathode Plane Assemblies (CPA)
  Resistive Kapton laminated on dielectric panels
  180 kV nominal (2 x 3.6 m drift @ 500 V/cm)
  Highest voltage in all LArTPCs to date

## Slide 4: ProtoDUNE: How does it work?
Cartoon animation made by Bo Yu (BNL)
Ionization electrons drifted and induced current read out by three wire planes
Scintillation light collected by photon detection system
  Providing event t0

## Slide 5: General Overview of LArTPC Reconstruction
LArTPC Signal Formation
Noise Filtering & Signal Processing
deconvolving
Kinematic Recon.
2D Matching / 3D Recon.
dE/dx & PID
Imaging, pattern recognition, clustering, etc.
imaging
fitting
T17.00007, Heng-Ye Liao
ProtoDUNE Proton Analysis
Main focus of today’s talk
Induction
collection
1 GeV
Cosmic
Preliminary Result

## Slide 6: Noise Filtering
Filter out external noise properly
Correct additional hardware effect/distortion
After noise filtering
“50 kHz” collection plane noise
Coherent noise
Time [0.5us]
Channel
Channel
Time [0.5us]
clock issue in one of 120 FEMBs
“RC” undershoot
Before
After
After correction
Time [0.5us]
After correction

## Slide 7: Noise Filtering (cont’)
Fix some residual electronics issues
Overall performance of noise filtering is good
Sticky bits
“ledge” waveform
Excluded from signal processing
After noise filtering
ENC of collection (X) plane 565 ± 60 e-
ENC of induction (V) plane 662 ± 56 e-
ENC of induction (U) plane 651 ± 54 e-
evidence in ~3% of total channels
< 1% of total channels

## Slide 8: Field response: Garfield drift simulation
Garfield, a drift-chamber simulation program User’s Guide, Veenhof, R. (1993)
Electron drift path (E field)
+
Weighting potential
Ramo’s theorem
=
Weighting potential
Wire pitch direction
Drift direction
G
U
V
W
Ionization electrons
Charge deposit
Induced current
Long-range induction

## Slide 9: Field response: Garfield drift simulation
Field response in the central wire
Ramo’s theorem
=
W

## Slide 10: Field response: Garfield drift simulation
Central wire field response electronics response (preamp etc.)
Kernel in signal processing
Ramo’s theorem
=
W
W-wire

## Slide 11: Long-range Induction: 2-D deconvolution
It is natural to include the long-range induction effect in the deconvolution kernel
“2D” deconvolution (time + wire direction): M(t) -> S(t) through FFT
Equivalently, recover ionization charges from induced current from all wires
t: time, : wire
Ionization Electron Signal Processing in Single Phase LArTPCs I.
JINST 13 P07006 (2018)

## Slide 12: Signal Processing Example
Bipolar signal deconvolved into an unipolar charge distribution
Long tracks in drift direction are obscure in the induction waveform
  cancellation of successive bipolar signals recovered via the 2D deconvolution
After Noise Filtering
Time [s]
Topology dependence
wire 385
After 2-D Deconvolution
wire 385
wire 385
wire 385
Raw waveform
Deconvolved signal

## Slide 13: Track Reconstruction Example
3D view
Collection plane view
Time [s]
Wire No.
Induction U plane view
Wire No.
Time [s]
2 EM showers and a pion interaction with 4 outgoing particles
Three-plane “matching” solves the degeneracies inherent from wire readout ambiguity
Video | Online gallery by Chao Zhang (BNL)

## Slide 14: Summary
ProtoDUNE-SP has been successfully operated since late 2018
  Full-scale component design of the DUNE FD
The “2D” signal processing technique has been developed and successfully applied to the wire readouts
  High-quality noise filtering
  Field response kernel: Garfield electron drift simulation
  Long-range induction handled in the deconvolution
High-performance signal processing is essential to the downstream event reconstruction and physics analysis

## Slide 15: Backup Slides

## Slide 16: Goals and challenges
ProtoDUNE-SP goals:
- Validate the prototype production and installation procedures - Confirmation of the design and suggest improvements
- Test-beam data to calibrate the detector response to different particle species and to measure argon-hadrons cross sections - Demonstration of the long term stability of the detector
Challenges (not exhaustive list):
- Size and modularity: all components full size for DUNE-SP
- Cryostat: warm structure, passive insulation, LNG technology
- Purity: non-evacuable volume, piston purge, purification, …
- HV: highest voltage TPC ever operated, resistive cathode
- Stability: light scintillation, HV, purity, cold electronics, …

## Slide 17: Basics of (1D) Signal Processing
Principal method to extract wire charge S(t) is deconvolution
By given a response function R(t), signal S(t) can be easily derived via Fourier transform
A filter function F() introduced to suppress the big fluctuation after deconvolution
Fourier transform
Deconvolution + Filter
Inverse Fourier transform
Liquid Argon TPC Signal Formation, Signal Processing and Hit Reconstruction
Bruce Baller, JINST 12 (2017) no.07, P07010

## Slide 18
02/10/2018:
First event seen from beam!
(1 GeV electron)

## Slide 19
Beam halo (high energy) muon with bremsstrahlung initiated E.M. shower
Collection plane view

## Slide 20
Induction U plane view
Induction V plane view
Collection plane view
3D view

## Slide 21: A BNL contribution to ProtoDUNE SP: Cold Readout Electronics

## Slide 22: Integrated LAr-TPC Readout
cryostat
APA
Each APA is isolated inside the cryostat and only connected to the cryostat through the CE at its own CE flange.
Warm Interface Electronics: from CE to DAQ with shielding and local real-time diagnostics.
Feedthrough